## Slide 1: Content Classification Based on Objective Video Quality Evaluation for MPEG4 Video Streaming over Wireless Networks
Asiya Khan, Lingfen Sun
& Emmanuel Ifeachor
3rd July 2009
University of Plymouth
United Kingdom
{asiya.khan; l.sun; e.ifeachor} @plymouth.ac.uk
Information &
Communication
Technologies

## Slide 2: Presentation Outline
Background
    Current status and motivations
    Video quality for wireless networks
    Aims of the project
Main Contributions
    Classification of video contents based on
    objective video quality evaluation (MOS)
    Degree of influence of each QoS parameter
    Apply results to send bitrate control methods
Conclusions and Future Work

## Slide 3: Current Status and Motivations (1)
Perceived quality of the streaming videos is likely to be the
major determining factor in the success of the new multimedia
applications.
The prime criterion for the quality of multimedia applications is
the user’s perception of service quality.
Video transmission over wireless networks are highly sensitive
to transmission problems such as packet loss or network
delay.
It is therefore important to choose both the application level i.e.
the compression parameters as well as network setting so that
they maximize end-user quality.

## Slide 4: Current Status and Motivations (2)
Feature extraction is the most commonly used method to classify
videos
The limitation of feature extraction is that it does not express the
semantic scene importance
It is important to determine the relationship between the
users’ perception of quality to the actual characteristic of the
content and hence increase users’ QoS of video applications by
using priority control for content delivery networks
Hence the motivation of our work – to classify video contents according to video quality evaluation based on the MOS from quality degradations caused by a combination of application and network level parameters

## Slide 5: Video Quality for Wireless Networks
Video Quality Measurement
  Subjective method (Mean Opinion Score – MOS [1])
  Objective methods
      Intrusive methods (e.g. PSNR)
      Non-intrusive methods (e.g. regression-based models)
Why do we need to classify video content?
  Streaming video quality is dependent on the intrinsic attribute of the
  content.
  QoS of multimedia affected by both Application level and Network
  level parameters is dependent on the type of content
  Multimedia services are increasingly accessed with wireless
  components
  Once classification is carried out, Quality of Service (QoS) control can
  be applied to each content category depending on the initial encoding
  requirement

## Slide 6: Aims of the project
Classification of video content into three main categories
based on objective video quality assessment (MOS)
Compare the classification model to spatio-temporal grid
Find the degree of influence of each QoS parameter
Find the relationship between video contents and objective
video quality in terms of prediction models
Apply results to send bitrate control from content providers
point of view

## Slide 7: Simulation Set-up
  CBR background traffic
  1Mbps Mobile Node
  11Mbps
  Video Source
  10Mbps, 1ms
  transmission rate
All experiments conducted with open source Evalvid [3] and NS2 [4]
Random uniform error model
No packet loss in the wired segment
MPEG4 codec open source ffmpeg [2]

## Slide 8: List of Variable Test Parameters
  Application Level Parameters:
      Frame Rate FR (10, 15, 30fps)
      Spatial resolution QCIF (176x144)
      Send Bitrate SBR (18, 44, 80, 104, & 512kb/s)
  Network Level Parameters:
      Packet Error Rate PER (0.01, 0.05, 0.1, 0.15, 0.2)

## Slide 9: Simulation Platform
  Video quality measured by taking average PSNR over all
  the decoded frames.
  MOS scores calculated from conversion from Evalvid[3].
PSNR(dB) | MOS
> 37 | 5
31 – 36.9 | 4
25 – 30.9 | 3
20 – 24.9 | 2
< 19.9 | 1

## Slide 10: Classification of video contents (1)
  End-to-end perceived video quality
  Raw video PSNR/MOS Degraded video
  Raw video Received video
Simulated system
Application Parameters Network Parameters Application Parameters
Video quality: end-user perceived quality (MOS), an important metric.
Affected by application and network level and other impairments.
Video quality measurement: subjective (MOS) or objective (intrusive or non-intrusive)
Full-ref Intrusive Measurement
Encoder
Decoder

## Slide 11: Classification of video contents (2)
MOS MOS
Application Level
SBR, FR
Network Level
PER
Content type estimation
Content type
Video MOS Scores(obtained by objective evaluation)
A total of 450 samples were generated based on NS2 and Evalvid for content classification.

## Slide 12: Classification of video contents (3)
- Data split at 62% (from 13-dimensional Euclidean space)
- Cophenetic Coefficient C ~ 73.29%
- Classified into 3 groups as a clear structure is formed

## Slide 13: Classification of Video Contents (4)
  Test Sequences Classified into 3 Categories of:
  Slow Movement(SM)
  (news type of videos e.g. video-
  conferencing application)
  Gentle Walking(GW)
  (wide-angled clips in which both
  background and content is moving
  e.g. typical video call application)
  Rapid Movement(RM) –
  (sports type clips – e.g. typical video streaming application will
  have all three types of content)

## Slide 14: Comparison of the Classification model with S-T dynamics
Low spatial – Low temporal activity: defined in the bottom left quarter in the grid.
Low spatial – High temporal activity: defined in the bottom right quarter in the grid.
High spatial – High temporal activity: defined in the top right quarter in the grid.
High spatial – Low temporal activity: defined in the top left quarter in the grid.

## Slide 15: Principal Co-ordinate Analysis
The scatter plot of the points provides a visual representation of the original distances and produces representation of data in a small number of dimensions.
The distance between each video sequence indicates the characteristics of the content, e.g. the closer they are the more similar they are in attributes.

## Slide 16: Degree of influence of each QoS parameter
Content type | Content | Scores | SBR | FR | PER
SM | Akiyo | 0.212 | 0.57 | -0.58 | -0.58
 | Suzie | 0.313 | 0.66 | 0.25 | -0.71
 | Grandma | 0.147 | -0.76 | 0.64 | -0.05
 | Bridge-close | 0.092 | 0.41 | -0.22 | -0.89
GW | Table Tennis | 0.287 | 0.08 | -0.99 | 0.11
 | Carphone | 0.154 | 0.35 | -0.93 | 0.10
 | Tempete | 0.231 | 0.25 | -0.46 | -0.85
 | Foreman | 0.204 | 0.56 | 0.45 | -0.69
 | Coastguard | 0.221 | 0.62 | -0.60 | 0.51
RM | Stefan | 0.413 | 0.40 | -0.72 | 0.58
 | Football | 0.448 | 0.62 | -0.57 | 0.55
 | Rugby | 0.454 | 0.65 | -0.59 | 0.48
Principal component scores table

## Slide 17: Degree of influence of each QoS parameter
From the PCA scores table , we find that:
Content type 1 – SM: The main factors degrading objective video quality are:
    Frame rate and
    Send bitrate.
However, the requirements of frame rate are higher than that of send bitrate.
Content type 2 – GW: The main factors degrading objective video quality are:
    Send bitrate and
    Packet error rate.
In this category packet loss has a much higher impact on quality compared to SM.
Content type 3 – RM: The main factor degrading the video quality are:
    Send bitrate and
    Packet error rate.
Same as GW.

## Slide 18: Degree of influence of each QoS parameter
Degree of influence of QoS Parameters given by the Box plot
From the Box and Whiskers plot:
For SM FR has a bigger impact
on quality
For GW PER has a bigger
impact than SBR and FR
Similarly, SBR and PER have bigger impact for RM

## Slide 19: Relationship between video contents and objective video quality
  Proposed Model for SM, GW, RM
MOSSM = 0.0075SBR – 0.014FR - 3.79PER + 3.4 Content type: SM (R2 = 85.72%) MOSGW = 0.0065SBR – 0.0092FR – 5.76PER + 2.98 Content type: GW (R2 = 99.65%) MOSRM = 0.002SBR – 0.0012FR - 9.53PER+ 3.08 Content type: RM (R2 = 89.73%)

## Slide 20: Evaluation of the proposed models (1)
  The application of the proposed models in content delivery networks
  From a content providers point of view, the equations
  proposed in the model can be used to calculate the minimum
  send bitrate for a video sequence for a given content type
  that will give minimum acceptable quality.
  Hence the content provider can specify the quality, video send
  bitrate can be reduced or increased according to the content type
  while keeping the same objective video quality.

## Slide 21: Evaluation of the proposed models (2)
  Predicted SBR values for specific quality levels
Content type | FR | PER | MOSgiven | SBR (Kbps) Predicted
SM | 10 | 0 | 3.5 | 20
 | 15 | 0 | 3.6 | 55
 | 30 | 0/0.05 | 3.8 | 75/135
GW | 10 | 0 | 3.7 | 125
 | 15 | 0 | 3.9 | 165
 | 30 | 0/0.02 | 4.1 | 215/235
RM | 10 | 0 | 3.8 | 360
 | 15 | 0 | 4.1 | 500
 | 30 | 0/0.02 | 4.2 | 580/700
Predicted Send Bitrate Values for Specific Quality Levels

## Slide 22: Conclusions
  Classified the video content into three categories using
  objective video quality evaluation.
  The classified video contents compare well to the spatio-
  temporal grid.
  Further found the degree of influence of each QoS parameters
  on quality in terms of PCA and Box plots.
  QoS parameters of PER are most important for content types
  of GW and RM, whereas FR is more important for SM
  Captured the relationship between video contents and objective
  video quality in terms of multiple linear regression analysis
  Applied the results to send bitrate control from content
  providers point of view

## Slide 23: Future Work
  Extend to Gilbert Eliot loss model.
  Currently limited to simulation only.
  Extend to test bed based on IMS.
  Use subjective data for evaluation.
  Propose adaptation mechanisms for QoS control.

## Slide 24: References
  Selected References
ITU-T. Rec P.800, Methods for subjective determination of transmission quality, 1996.
Ffmpeg, http://sourceforge.net/projects/ffmpeg
J. Klaue, B. Tathke, and A. Wolisz, “Evalvid – A framework for video transmission and quality evaluation”, In Proc. Of the 13th International Conference on Modelling Techniques and Tools for Computer Performance Evaluation, Urbana, Illinois, USA, 2003, pp. 255-272.
NS2, http://www.isi.edu/nsnam/ns/.

## Slide 25: Contact details
http://www.tech.plymouth.ac.uk/spmc
Asiya Khan asiya.khan@plymouth.ac.uk
Dr Lingfen Sun l.sun@plymouth.ac.uk
Prof Emmanuel Ifeachor e.ifeachor@plymouth.ac.uk
http://www.ict-adamantium.eu/
Any questions?
Thank you!