## Slide 1: Content Clustering Based Video Quality Prediction Model for MPEG4 Video Streaming over Wireless Networks
Asiya Khan, Lingfen Sun
& Emmanuel Ifeachor
16th June 2009
University of Plymouth
United Kingdom
{asiya.khan; l.sun; e.ifeachor} @plymouth.ac.uk
Information &
Communication
Technologies

## Slide 2: Presentation Outline
Background
    Current status and motivations
    Video quality for wireless networks
    Aims of the project
Main Contributions
    Classification of video content into three main
    categories.
    Video quality prediction model from both
    application and network level parameters
Conclusions and Future Work

## Slide 3: Current Status and Motivations (1)
Perceived quality of the streaming videos is likely to be the
major determining factor in the success of the new multimedia
applications.
The prime criterion for the quality of multimedia applications is
the user’s perception of service quality.
Video transmission over wireless networks are highly sensitive
to transmission problems such as packet loss or network
delay.
It is therefore important to choose both the application level i.e.
the compression parameters as well as network setting so that
they maximize end-user quality.

## Slide 4: Current Status and Motivations (2)
Lack of efficient non-intrusive video quality measurement methods
Current video quality prediction methods mainly based on application or network level parameters
Hence the motivation of our work – to predict video quality using a combination of both application and network level parameters for all content types.

## Slide 5: Video Quality for Wireless Networks (1)
Video Quality Measurement
  Subjective method (Mean Opinion Score – MOS [1])
  Objective methods
      Intrusive methods (e.g. PSNR)
      Non-intrusive methods (e.g. regression-based models)
Why do we need to predict video quality?
  Streaming video quality is dependent on the intrinsic attribute of the
  content.
  QoS of multimedia is affected by both the Application level and Network
  level parameters
  Multimedia services are increasingly accessed with wireless
  components
  For Quality of Service (QoS) control for multimedia applications

## Slide 6: Video Quality for Wireless Networks(2)
  End-to-end perceived video quality
  Raw video PSNR/MOS Degraded video
  Raw video Received video
Simulated system
Application Parameters Network Parameters Application Parameters
Video quality: end-user perceived quality (MOS), an important metric.
Affected by application and network level and other impairments.
Video quality measurement: subjective (MOS) or objective (intrusive or non-intrusive)
MOS
Full-ref Intrusive Measurement
Encoder
Decoder
Ref-free Non-Intrusive Measurement

## Slide 7: Aims of the project
Classification of video content into three main categories
Novel non-intrusive video quality prediction models based
on regression analysis in terms of MOS
Video Quality Modeling
Temporal Feature Extraction
Spatial Feature Extraction
Content Type
Estimation
PQoS
Model
CT, SBR, FR, …
Loss, Delay, Jitter
Network
MOS

## Slide 8: Classification of video contents (1)
Temporal Features:
Measured by the
movement in a clip and is
given by the SAD(Sum of
Absolute Difference) value.
Spatial Featues:
Blockiness, blurriness,
brightness between the
current and previous frames.
Content type estimation:
Hierarchical and K-means
cluster analysis.
Temporal Feature Extraction
Spatial Feature Extraction
Content type estimation
Content type
Raw Video

## Slide 9: Classification of video contents (2)
- Data split at 38%
- Cophenetic Coefficient C ~ 86.21%
- Classified into 3 groups as a clear structure is formed

## Slide 10: Classification of Video Contents (4)
  Test Sequences Classified into 3 Categories of:
  Slow Movement(SM)
  (news type of videos)
  Gentle Walking(GW)
  (wide-angled clips in which both
  background and content is moving)
  Rapid Movement(RM) –
  (sports type clips)
  All video sequences were in the qcif format (176 x 144), encoded with MPEG4 video codec[2]

## Slide 11: Simulation Set-up
  CBR background traffic
  1Mbps Mobile Node
  11Mbps
  Video Source
  10Mbps, 1ms
  transmission rate
All experiments conducted with open source Evalvid [3] and NS2 [4]
Random uniform error model
No packet loss in the wired segment

## Slide 12: List of Variable Test Parameters
  Application Level Parameters:
      Frame Rate FR (10, 15, 30fps)
      Spatial resolution QCIF (176x144)
      Send Bitrate SBR (18, 44, 80kb/s for SM; 44, 80,
      128 for GW; 104, 384 & 512kb/s for RM)
  Network Level Parameters:
      Packet Error Rate PER (0.01, 0.05, 0.1, 0.15, 0.2)

## Slide 13: Simulation Platform
  Video quality measured by taking average PSNR over all
  the decoded frames.
  MOS scores calculated from conversion from Evalvid[3].
PSNR(dB) | MOS
> 37 | 5
31 – 36.9 | 4
25 – 30.9 | 3
20 – 24.9 | 2
< 19.9 | 1

## Slide 14: Novel Non-intrusive Video Quality Prediction Model
  Regression-based Prediction Model
  FR
  SBR
  Video CT
  MOS
  PER
Application Level
Network Level
Ref-free Prediction Model
Content Type
A total of 450 samples were generated based on Evalvid[2] for testing and 210 samples as the validation dataset for the 3 CTs.

## Slide 15: PCA Analysis
The PCA results show the influence of the chosen parameters (SBR, FR and PER) on our data set for the three content types of SM, GW and RM.

## Slide 16: Proposed Model
FR (Frame Rate), SBR (Send Bit Rate ), PER (Packet Error Rate)
Coeff | Slow movement (SM) | Gentle Walking (GW) | Rapid movement (RM)
a1 | 4.5796 | 3.4757 | 3.0946
a2 | -0.0065 | 0.0022 | -0.0065
a3 | 0.0573 | 0.0407 | 0.1464
a4 | 2.2073 | 2.4984 | 10.0437
a5 | 7.1773 | -3.7433 | 0.6865

## Slide 17: Novel Non-intrusive Video Quality Prediction Model
  Evaluation of the Proposed Model for SM, GW, RM
 | SM | GW | RM
R2 | 79.9% | 93.36% | 91.7%
RMSE | 0.2919 | 0.08146 | 0.2332

## Slide 18: Conclusions
  Classified the video content into three categories.
  Proposed a reference free model for video quality
  prediction.
  Model based on a combination of Application and
  Network Level parameters of SBR, FR and PER.
  Carried out PCA to verify the choice of parameters.
  Obtained good prediction accuracy (between 80-94%
  for all contents).

## Slide 19: Future Work
  Extend to Gilbert Eliot loss model.
  Currently limited to simulation only.
  Extend to test bed based on IMS.
  Use subjective data for evaluation.
  Propose adaptation mechanisms for QoS control.

## Slide 20: References
  Selected References
ITU-T. Rec P.800, Methods for subjective determination of transmission quality, 1996.
Ffmpeg, http://sourceforge.net/projects/ffmpeg
J. Klaue, B. Tathke, and A. Wolisz, “Evalvid – A framework for video transmission and quality evaluation”, In Proc. Of the 13th International Conference on Modelling Techniques and Tools for Computer Performance Evaluation, Urbana, Illinois, USA, 2003, pp. 255-272.
NS2, http://www.isi.edu/nsnam/ns/.

## Slide 21: Contact details
http://www.tech.plymouth.ac.uk/spmc
Asiya Khan asiya.khan@plymouth.ac.uk
Dr Lingfen Sun l.sun@plymouth.ac.uk
Prof Emmanuel Ifeachor e.ifeachor@plymouth.ac.uk
http://www.ict-adamantium.eu/
Any questions?
Thank you!